## Slide 1: Final Project: Branch Prediction
Paul-John Clet
ECSE 6680 – Advanced VLSI Design | 04/18/24

## Slide 2
Agenda
Introduction
What is branch prediction?
Why is it useful?
System Architecture
High level design
Component analysis
Testing
RISC-V code
Testbench and results
Conclusion
Future work

## Slide 3
What is Branch Prediction?
  Branch Prediction (BP) – Technique used in CPU design to guess the outcome of a conditional statement before it is calculated [1]
  Essentially decide to take a branch/jump based on the PC and branch history
  Various forms of dynamic branch predictors:
    1-bit predictors – for each branch, remember the last outcome
    2-bit predictors – introduce strong/weak taken and not taken
    2-level predictors – introduce a global history
  Figure 1: Single bit predictor example [2]

## Slide 4
Why is it Useful? (1)
  This project’s design uses a simplified 3 stage RISC-V processor architecture
  Leverage branch prediction to minimize the number of clock cycles lost
  Potential to save many clock cycles in a modern CPU
  Figure 2: 3 stage RISC-V processor pipeline stages with branch prediction
Notes: Show cycles here

## Slide 5
Why is it Useful? (2)
  4 cases for a branch/jump instruction
  With BP, the penalty is on the cases where branch prediction is incorrect
  Can rely on branch prediction for saving cycles
  Modern branch predictors have >95% accuracy [2]
Prediction | Actual | Number of Clock Cycles Lost | 
 |  | Without BP | With BP
Not Taken | Not Taken | 0 | 0
Not Taken | Taken | 2 | 2
Taken | Not Taken | 0 | 2
Taken | Taken | 2 | 0
Notes: Show cycles here

## Slide 6
Agenda
Introduction
What is branch prediction?
Why is it useful?
System Architecture
High level design
Component analysis
Testing
RISC-V code
Testbench and results
Conclusion
Future work

## Slide 7
High Level Architecture
  8 individual modules designed (+2 for testbench and toplevel)
  4 modules for RISC-V CPU pipeline
    Program Counter (PC)
    Instruction Queue
    Instruction Decode Pipeline
    Execution Pipeline (Includes EX+WB stages)
  4 modules for BP
    Global Branch History Register (GHR)
    Gskew Predictor
    Branch Target Buffer
    Prediction Validation
  Figure 3: Simplified system for branch prediction, including all modules

## Slide 8
Branch Prediction Component Analysis
  Focus on Branch Predictor Architecture and Functionality
  Prediction Steps:
  Get GHR and PC bits
  Decide if the branch is taken based on Gskew predictor (next slide)
  Check if there is a hit in the BTB
  If and only if both are true, output true to PC, taking the BTB address
  Figure 4: Branch prediction modules and general functionality

## Slide 9
Component Analysis – Gskew Predictor
  Use a 2-bit PHT with entries (k=3), we store the recent branch decisions
  Idea: Utilize 3 hash functions for the pattern history table, then take a majority vote
  bimodal – last k bits of PC
  Gselect – concat(PC[k-1:0], GHR[0])
  Gshare – XOR(PC[k-1:0], GHR[k-1:0])
  Figure 5: Gskew predictor module breakdown [3]

## Slide 10
Agenda
Introduction
What is branch prediction?
Why is it useful?
System Architecture
High level design
Component analysis
Testing
RISC-V code
Testbench and results
Conclusion
Future work

## Slide 11
Test Code (1)
  Goal: Use branch instructions, show performance with/without successful BP
  Figure 6: Original RISC-V code for testing BP
  Figure 7: Converted code flow chart

## Slide 12
Test Code (2)
  Translate and load all the instructions
    Follow RISC-V architecture with 3 types of instructions: R, SB, UJ
  Pre-load the Branch Target Buffer
    Load the two branch addresses in at their respective addresses
  Pre-load the PHT
    Set each of the 8 entries to 10 (Weak taken)
  Figure 9: Input to the Branch Target Buffer, allowing the two branch instructions to jump to each other
  Figure 8: Breakdown for each instruction in RISC-V

## Slide 13
Simulation Results (1)
  Partial console output from ModelSim with branch always taken
IF
IF
3 4 5
ID
Clock Cycle
Instr
add r2, r2, r1
bne r2, r10, loop2
nop
EX
ID
ID
EX
  Figure 10: ADD and BNE instructions successful output
Notes: Show cycles here

## Slide 14
Simulation Results (2)
  Figure 11: Simulation results without branch prediction (109 cycles to completion)
  Figure 12: Simulation results with branch prediction (86 cycles to completion)
  Without Branch Prediction
  With Branch Prediction
  Saved 23 clock cycles – 21% reduction
  Can have much greater reduction based on the number of pipeline stages
  Can also have negative impacts based on the program and prediction accuracy
Notes: Show cycles here

## Slide 15
Agenda
Introduction
What is branch prediction?
Why is it useful?
System Architecture
High level design
Component analysis
Testing
RISC-V code
Testbench and results
Conclusion
Future work

## Slide 16
Conclusion and Future Work
  Combined Gskew predictor with BTB to perform branch prediction at the IF stage
  Designed a program to test branch prediction functionality using RISC-V ISA
  Achieved at 21% runtime reduction with a 3-stage pipeline with potential to save many cycles in a modern CPU
  Future Work
  Fully implement updates to PHT
  Extend to a longer and more complex pipeline to see full benefits
  Implement more instructions and instruction types, allowing for more complex programs to be executed

## Slide 17
References
  [1] What is a Branch Prediction, “What is a Branch Prediction?,” Computerhope.com, 2017. https://www.computerhope.com/jargon/b/branch-prediction.htm
  ‌[2] L. Liu, Class Lecture, Topic: “Advanced Computer Architecture: Branch Prediction.”, ECSE 4780/6700, College of Engineering, Rensselaer Polytechnic Institute, Troy, NY, Mar. 2024.
  [3] L. Liu, Class Lecture, Topic: “Advanced Computer Architecture: Branch Prediction II.”, ECSE 4780/6700, College of Engineering, Rensselaer Polytechnic Institute, Troy, NY, Mar. 2024.
  [4] ltziyan He, “Design a Three-Stage Pipelined RISC-V Processor Using SystemVerilog KTH Thesis Report.” Available: https://www.diva-portal.org/smash/get/diva2:1713647/FULLTEXT01.pdf
  ‌[5] Mutlu, “8-740/640 Computer Architecture Lecture 5: Advanced Branch Prediction,” 2015. Accessed: Apr. 12, 2024. [Online]. Available: https://course.ece.cmu.edu/~ece740/f15/lib/exe/fetch.php?media=18- 740-fall15-lecture05-branch-prediction-afterlecture.pdf
  ‌
Notes: https://www.educative.io/answers/what-is-branch-prediction
#] Lecturer(s) Initial(s). Surname(s), Class Lecture, Topic: "Lecture title.” Unit Code, College/Faculty, University, Location, Abbrev. Month, Day, Year.
Referencing elements to cite:
[#] Reference number (matching the in-text citation number)
Lecturer’s first initial. Lecturer’s second initial, if provided. Lecturer’s last name
Class Lecture
Topic: Lecture title in lower case
Unit Code
College/Faculty
Location: City
Abbrev. Month, Day, Year. Refer to the Abbreviated month section for further information
[1] H. King, Class Lecture, Topic: "Lecture 3- AC Circuits." NEF2251/VAM3112, College of Engineering and Science, Victoria University, Melbourne, Vic., Apr. 2016.